Specifications of 1/3” SONY Effio CCD（673+4140）

| ITEM: | Specification |
| --- | --- |
| Configuration scheme: | 1/3” SONY Effio CCD（673+4140） |
| Image Sensor: | 1/3” SONY CCD |
| Total pixels: | PAL 1020H×596V NTSC 1020H×508V |
| Effective Pixels: | PAL 976H×582V NTSC 976H×494V |
| TV System: | PAL/NTSC |
| Resolution: | 700TVL |
| Digital noise reduction: | 2DNR, 16 level support for 0~15 adjustable |
| Minimum Illumination: | 0.01Lux/F1.2 |
| Signal to noise ratio: | ≥48dB |
| Video Output: | 1.0Vp-p/75Ω |
| Automatic gain control: | 0.25/0.5/0.75/1 four level adjustable, The maximum can reach 55dB |
| Backlight compensation: | High brightness backlight compensation (HLC) / backlight compensation |
| Exposure mode: | electronic exposure |
| Electronic shutter: | 1/50(1/60) - 1/100000 second |
| Gamma correction: | 0.45/1.0 |
| Working voltage: | DC12V±5% |
| Working temperature: | -20℃-60℃ RH95% Max |
| Storage temperature: | -30℃-80℃ RH95% Max |
| Lens: | 2.5mm/2.8mm/3.6mm (optional) |
| Microphone: | Optional |
| Output connector: | RCA(AV)/Aviation/S-Video/BNC (optional) |
| Lightning protection: | YES |